## Slide 1: RTT independence in TCP Prague
Olivier Tilmans <olivier.tilmans@nokia-bell-labs.com>
Koen De Schepper <koen.de_schepper@nokia-bell-labs.com>
20-02-2020, TSVWG interim

## Slide 2
Queuing delays act as cushion
The throughput of competing AIMD flows depends on their RTT ratio
 | qdelay | Throughput imbalance
Taildrop | 200ms | 
PIE | 15ms | 
Codel | 5ms | 
L4S AQM | 500us | 
 | qdelay | Throughput imbalance
Taildrop | 200ms | 
PIE | 15ms | 
Codel | 5ms | 
L4S AQM | 500us | 
Assuming two flows with base RTT of 15ms and 0.5ms, and a constant marking probability
or

## Slide 3
DualQ also gives a different Q per traffic class
The throughput of competing AIMD flows depends on their RTT ratio
 | Base RTT | Throughput imbalance
DualQ | 200ms | 
DualQ | 15ms | 
DualQ | 5ms | 
DualQ | 500us | 
 | Base RTT | Throughput imbalance
DualQ | 200ms | 
DualQ | 15ms | 
DualQ | 5ms | 
DualQ | 500us | 
Assuming DualQ with targets of 15ms and 0,5ms, equal base RTT and a window-fair coupling (k=2)
or

## Slide 4
Code to be released soon (demo available)
New Prague add-on to steer RTT dependence
New Prague CC can have with a target RTT function that can represent any constant or function of flow state
For example resulting in:
 | Base RTT | Throughput imbalance
DualQ | 200ms | 
DualQ | 15ms | 
DualQ | 5ms | 
DualQ | 500us | 
 | Base RTT | Throughput imbalance
DualQ | 200ms | 
DualQ | 15ms | 
DualQ | 5ms | 
DualQ | 500us | 

## Slide 5
Smart f()
(Long term) Throughput balance with other RTT flows
Accelerate faster
at small RTTs
Handle
shorter flows
faster
IETF or applications
to decide?

## Slide 6
Key changes to TCP Prague
Controlled RTT dependence in TCP Prague
We control Additive Increase to behave as a target RTT flow
  Trigger the same amount/frequency of marks as a target RTT flow
We leave the Multiplicative Decrease unchanged
  Preserve responsiveness as much as possible to preserve latency
Control the EWMA update frequency on the target RTT independently from the e2e RTT
  Ensure that different RTT flows can converge to the same alpha, even on a step

## Slide 7
Other changes to TCP Prague
Switch to unsaturated marking by default, i.e., cwnd growth is , regardless of the congestion state (TCP_CA_CWR, …)
Generalize fixed-point cwnd manipulation, e.g., carry over remainders from successive cwnd increases and reductions
Align to to support unsaturated signal and smoother throughput
The marking probability is usually too low (e.g., 3%) to yield a single packet reduction
and the increments can become less than a packet per RTT

## Slide 8
Demo/video
f(rtt)= (rtt + 15ms)
Code available in https://github.com/L4STeam/linux RTT dependence can be controlled with the prague_rtt_* module parameters, e.g.,
`echo 3 | sudo tee /sys/module/tcp_prague/parameters/prague_rtt_scaling`

## Slide 9
Baseline—Prague vs Cubic
Test results—100Mbit/s bottleneck, increasing base RTTs

## Slide 10
Prague [ f(rtt) = max(15ms, rtt) ] vs Cubic
Test results—100Mbit/s bottleneck, increasing base RTTs

## Slide 11
Prague [ f(rtt) = rtt + 15ms ] vs Cubic
Test results—100Mbit/s bottleneck, increasing base RTTs

## Slide 12
Prague [ f(rtt) = max(15ms, rtt) ] vs Prague
Test results—100Mbit/s bottleneck, mixed base RTTs

## Slide 13
Baseline—Prague vs Cubic
Test results—100Mbit/s bottleneck, increasing base RTTs

## Slide 14
Prague [ f(rtt) = max(15ms, rtt) ] vs Cubic
Test results—100Mbit/s bottleneck, increasing base RTTs

## Slide 15
Prague [ f(rtt) = rtt + 15ms ] vs Cubic
Test results—100Mbit/s bottleneck, increasing base RTTs

## Slide 16
Prague [ f(rtt) = max(15ms, rtt) ] vs Prague
Test results—100Mbit/s bottleneck, mixed base RTTs